## Slide 1: Op Amp: Nearly ideal differential voltage amplifier
Ideal op-amp:
A 
Rin 
Rout0

## Slide 2: Before you build a circuit, you need to draw circuit diagram, and a wiring diagram
This is a circuit diagram:
Wiring diagram includes the connections specific pins on the chip,
and to the power supplies

## Slide 3: This is a wiring diagram for non-inverting amplifier
Input signal
Ground
Output
to oscilloscope
Ground
V+
V -
R1
R2

## Slide 4: Inverting amplifier
-
+
v1
v2
+
Vout
-
R1
+
-
vs
R2
This amplifier works as designed provided Vout is in the range
between V- and V+
Clipping of output signal occurs when the amplitude of Vout is too high

## Slide 5: Summing amplifier
-
+
+
vout
-
R1
R f
vS1
- +
- +
vS2
R2
Vout= - Rf (VS1/R1+VS2/R2)

## Slide 6: Different pulse shapes can be observed when we add harmonics to sinusoidal signals
clear
t=0:1000;
omega=2*pi/200;
V1=cos(omega*t)-(1/3)*cos(3*omega*t)
+(1/5)*cos(5*omega*t);
figure(1);plot(t,V1)
With large number of harmonics
the output approaches the
square wave

## Slide 7: Different pulse shapes can be observed when we add harmonics to sinusoidal signals
clear
t=0:1000;
omega=2*pi/200;
V1=cos(omega*t)+(1/3)*cos(3*omega*t)
+(1/5)*cos(5*omega*t);
figure(1);plot(t,V1)
With large number of harmonics
the output approaches the
triangular wave

## Slide 8: All real amplifiers have a finite bandwidths
Important trade off:
Gain * Bandwidth is approximately a constant
Bandwidth is the range of frequencies
for which the device works properly
Our OpAmp circuits work well for low frequencies, down to DC
Bandwidth in this case is defined as the frequency
for which the output power gain is down to 50%
of the design value